## Slide 1
Chapter 1 Introduction
Computer Networking: A Top Down Approach
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016

## Slide 2: Chapter 1: roadmap
  1.0 a little history
  1.1 what is the Internet?
  1.2 network core - packet switching
  1.3 the global Internet infrastructure
  1.4 network architecture - protocol layers
  1.5 a primer on Internet addressing
  1.6 networks under attack - security
Notes: 2

## Slide 3: Internet history
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet - Advanced Research Projects Agency Network
1969: first ARPAnet node to node transmission (50yrs ago!)
  UCLA to Stanford – first message attempt was a remote login – lo(gin)
“The first-ever computer-to-computer link was established on ARPAnet, the precursor to the Internet, on October 29, 1969”
Grew to 4 nodes UCLA, SRI, UCSB, Utah by end of 1969
1972:
  ARPAnet expands to 15 nodes
  ARPAnet public demo
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
1973:
  ARPAnet goes international
1961-1972: Early packet-switching principles

## Slide 4
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
Late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets
1979: ARPAnet has 200 nodes
1980: ARPAnet first outage due to a ”virus”
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
defines today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets
Internet history

## Slide 5
1981-82: early definition/testing of TCP/IP (based on Cerf and Kahn’s work) – end- to- end transport layer
1983: deployment of TCP/IP on ARPAnet
1982: smtp -e-mail protocol- defined
1983: DNS – host name to IP address translation- defined
1985: ftp -file transfer protocol- defined
1987: first Cisco router
1988: TCP congestion control
new national networks: CSnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks
Internet history

## Slide 6
early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
backbone links running at Gbps
network security to forefront
est. 50 million host, 100 million+ users
development of IPv6 starts due to worries over limited address space with IPv4 and poor security
1990s, 2000s: commercialization, the Web, new apps
Internet history

## Slide 7
2005-present
deployment of IPv6 starts (2012) – 2020 only 20%
~5B devices attached to Internet (2016)
  smartphones and tablets
aggressive deployment of broadband access
increasing ubiquity of high-speed wireless access
emergence of online social networks:
  Facebook: ~ one billion users
service providers (Google, Microsoft) create their own networks
  bypass Internet, providing “instantaneous” access to search, video content, email, etc.
e-commerce, universities, enterprises running their services in “cloud” (e.g., Amazon EC2)
Internet history

## Slide 8: Chapter 1: roadmap
  1.0 a little history
  1.1 what is the Internet?
  1.3 network core - packet switching
  1.5 the global Internet infrastructure
  1.4 network architecture - protocol layers
  1.5 a primer on Internet addressing
  1.6 networks under attack - security
Notes: 8

## Slide 9
Internet “network of networks”
  interconnected networks transport data between edge devices
  -> hardware
    switches, communication links that interconnect edge devices
  -> software
    network apps that facilitate the data exchange between edge devices
Internet standards
  IETF: Internet Engineering Task Force
    RFC: Request for comments
  IEEE: Inst. of Electrical & Electronic Eng.
  ITU: Intl Telecomm. Union (UN)
What’s the Internet: “the big picture”
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 10: What’s the Internet: a “nuts and bolts” view
billions of connected computing devices:
  hosts = end systems
  running software - network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
switches: forward chunks of data (packets)
  routers and switches
wired
links
wireless
links
router
smartphone
PC
server
wireless
laptop
mobile network
global ISP
regional ISP
home
network
institutional
network
components
configurations
Notes: 10

## Slide 11: What’s the Internet: a “service” view
an infrastructure that provides services to applications:
  Web, VoIP, email, games, e-commerce, social nets, …
it provides programming interface (API) to apps
  software modules (socket) that allow sending and receiving application programs to “connect” to Internet (via the network apps)
  service options (options/choices) necessary for the functionality of applications
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 12: Network Structure
network edge:
  hosts: clients and servers generate data
    servers often in data centers
    clients at the edge
access networks:
  serve to connect edge devices to the network
  mobile access networks
  residential access nets
  institutional access networks (school, company)
physical media:
  wired, wireless
  communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home/residential
network
institutional
network

## Slide 13: Transport of Data
Communication norms for interactions
  when humans or devices communicate, they generally follow a set of rules – referred to as a protocol - to exchange data
human protocols
Will differ dependent on
participants
different ages
backgrounds
languages
customs
…..
setting
a courtroom
a meeting
in a classroom
Introductions
……
Internet protocols
Will differ dependent on
type of devices
  hosts
  servers
  sensors
  mobile phones
  ……..
application
  queries
  downloads
  Sharing
  ……

## Slide 14
a human protocol a network protocol
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
What is a protocol?
Bye
Bye
Disconnect
Disconnect
protocols define the format and order of messages and the actions taken on message transmission and receipt
Notes: Courtroom, dinner table……

## Slide 15: Analogy: Internet – Postal Service
Internet: transmission of data from a source to a destination
  can have several hops on the way
  can require special handling
  can cost money – varies (free service, provider cost, per bit fee)
Postal service: transmission of mail from a source to a destination
  can have several hops on the way
  can require special handling
  cost money – varies (basic stamp, extra: weight, services)

## Slide 16: Postal Service/Internet Analogy
From address
To address
Stamp
Letter  Data
Delivery  Transmission
Postal Service Rules  Internet Rules
Envelope  Packet
Delivery Options
(registered, certified, priority)
 Trans. Options
(error control, priority)
Notes: Service Options: first class, registered, 2-day delivery….. Trans options: priority, guaranteed error free, high speed….

## Slide 17: Chapter 1: roadmap
  1.0 a little history
  1.1 what is the Internet?
  1.2 network core - packet switching
  1.3 the global Internet infrastructure
  1.4 network architecture - protocol layers
  1.5 a primer on Internet addressing
  1.6 networks under attack - security
Notes: 17

## Slide 18: The network core
mesh of interconnected switches referred to as routers
packet-switching: hosts break application-layer data into chunks and put into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity
  many end devices share network links

## Slide 19: End devices: generate data
every device, e.g. host, has a “network” address
address is used to find a receiving (aka destination) device
device sending function:
  takes application data
  breaks into smaller chunks, known as packets, of length L bits
  transmits packet into access network at transmission rate R
    link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet over link
L (bits)
R (bits/sec)
=
=

## Slide 20: Packet-switching: store-and-forward
store and forward: entire packet must arrive at router before it can be transmitted on next link – hop by hop
source
R bps
destination
1
2
3
L bits
per packet
R bps

## Slide 21: Packet Switching: queueing delay and loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
queueing delay and loss
if arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up
Impacts operation of protocols and service requirements of applications
Multiple sources share one output resource

## Slide 22: How do loss and delay occur?
A
B
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
packet being transmitted (trans delay)
packets queueing (queue delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 23: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 24
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
Four sources of packet delay
* Check out the Java applet for an interactive animation on trans vs. prop delay
dtrans and dprop
very different
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Notes: 24

## Slide 25: Queueing delay (revisited)
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
traffic intensity
= La/R
La/R ~ 0: avg. queueing delay small
La/R --> 1: avg. queueing delay large
La/R > 1: more “work” arriving
than can be serviced, average delay infinite!
average queueing delay
La/R ~ 0
La/R -> 1
* Check online interactive animation on queuing and loss
Need congestion control to stem flow – much like the highways

## Slide 26: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply
3 probes
3 probes
3 probes

## Slide 27: “Real” Internet delays, routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (router not replying)
trans-oceanic
link
* Do some traceroutes from exotic countries at www.traceroute.org
Notes: The source host will send out another ICMP request with higher TTL, it tries that several times till it gets a response or a destination unreachable error. If TTL exceeds max, it stops and ends the quest.

## Slide 28: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
* Check out the Java applet for an interactive animation on queuing and loss

## Slide 29: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 30: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 31: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput (for Z connections): min(Rc,Rs,R/Z)
in practice: Rc or Rs is often bottleneck link (<R) but if there are many connections sharing R, then R will be bottleneck
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 32: Chapter 1: roadmap
  1.0 a little history
  1.1 what is the Internet?
  1.2 network core - packet switching
  1.3 the global Internet infrastructure
  1.4 network architecture - protocol layers
  1.5 a primer on Internet addressing
  1.6 networks under attack - security
Notes: 32

## Slide 33: Internet structure: network of networks
end systems connect to Internet via access ISPs (Internet Service Providers)
  residential, company and university ISPs
access ISPs in turn must be interconnected via provider ISPs
  so that any two hosts can send packets to each other
  referred to as regional ISPs
  they in turn need to be interconnected…. by eventually backbone ISPs referred to as Tier 1 ISPs
hierarchy of interconnections  a global Internet
resulting “network of networks” is very complex
  evolution was driven by economics and national policies
let us take a stepwise approach to describe current Internet structure

## Slide 34: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
access
net
access
net
access
net
regional net
Each network is an Autonomous System (AS)
interconnected by gateway routers

## Slide 35: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
Content provider network
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services and content, close to end users – overlay networks.
IXP
Internet Exchange Point
IXP: Internet exchange point is the physical
infrastructure through which Internet service providers
(ISPs) and content delivery networks (CDNs) exchange
Internet traffic between their networks (autonomous systems).

## Slide 36: Internet structure: network of networks
at center: a small # of well-connected large networks
  “tier-1” backbone ISPs (e.g., Sprint, AT&T, Cox), national & international coverage
  content provider networks (e.g., Google) that connect their data centers to the Internet at various levels of the Internet hierarchy
IXP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
Regional ISP
Regional ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP

## Slide 37: Chapter 1: roadmap
  1.0 a little history
  1.1 what is the Internet?
  1.2 network core - packet switching
  1.3 the global Internet infrastructure
  1.4 network architecture - protocol layers
  1.5 a primer on Internet addressing
  1.6 networks under attack - security
Notes: 37

## Slide 38: Network Architecture
Networks are complex,
with many “pieces”:
  variety of edge devices
    different hardware/software
  variety of network devices
    routers, switches
  variety of physical media
  applications of all sorts
  protocols for data exchange
Question:
how should we organize such a complex system?
…. or at least our discussion of networks?

## Slide 39: Air travel – Tasks related to travel
a series of steps with distinct functionality at source step and corresponding destination step
Departures Process
(passenger dropoff
check-in, boarding pass)
baggage dropoff (label)
gates (load - priorities)
runway takeoff
Arrivals Process
(immigration,
customs, passenger
pickup)
baggage claim (label)
gates (unload – by rows)
runway landing
airplane routing
Source
Destination

## Slide 40: Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain?)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below

## Slide 41: Why layering?
dealing with complex systems:
layered structure allows breakdown of a complex system into smaller, well identified modules with explicit responsibilities/relationships to each other
  layered reference model – up/down relationships only - well defined
modularization eases maintenance/updating of system
  change of implementation of a layer’s service transparent to rest of system – internals are hidden
    e.g., change in gate procedure doesn’t affect rest of system operation, a flight is still a flight, passenger still gets to destination
    but a change in a layer’s service could impact performance of end system -> passengers may not be happy with a new gate procedure – unless reflected in their ticket purchase
layering considered harmful?
  Overlap in functionality (e.g., error control), dependency wrt specific requirements (e.g., timestamps) – not fully independent
Notes: Change runway, change airplane, change baggage carrousel….. It could impact “quality” of service, but you will still be serviced, changing implementation of layer is different than changing a service.

## Slide 42: Stack of tasks organized in layers
layered structure allows breakdown of a complex system into:
  smaller, well identified tasks
  with explicit responsibilities/relationships to each other
    generally – up/down relationships only
  eases maintenance/updating of system
    change in implementation of a layer’s task transparent to rest of system – internals are hidden
Notes: Change runway, change airplane, change baggage carrousel….. It could impact “quality” of service, but you will still be serviced, changing implementation of layer is different than changing a service.

## Slide 43: Is layering the right choice?
possible overlap in functionality (e.g., error recovery)
independence between layers hard to fully define –> a change in one layer’s responsibility may require an adjustment in another layer’s functionality
Notes: Change runway, change airplane, change baggage carrousel….. It could impact “quality” of service, but you will still be serviced, changing implementation of layer is different than changing a service.

## Slide 44: IETF* protocol stack - layers
application: supporting networked applications, process to process transfer – data stream  managed as messages
  FTP, SMTP, HTTP,…. – process id
transport: process to process message transfer  managed as segments
  TCP, UDP - port ids (216bits)
network: routing of data segments from source to destination device across the network (multi hop)  managed as datagrams
  IP - network address (4bytes x.y.z.a)
link: data transfer between neighboring devices (single hop)  managed as frames
  Ethernet, 802.11 (WiFi), PPP - hardware address (6octets)
physical: data “on the wire” managed as bits
  optical, electrical, electromagnetic….. - voltage levels, optical pulses…
application
transport
network
link
physical
*Internet Engineering Task Force created to oversee Internet development

## Slide 45: Layers: Functionality & Services
Data Link Layer: Transmission of frames
  Functions: Framing, link/hardware addressing, media access control, error checking, flow control
Network Layer: Forwarding of packets (datagrams)
  Functions: Network addressing, hop by hop routing, header checking, loop prevention
Transport Layer: Transfer of “chunks of application data”
  Functions: Connection establishment/termination, port id, error control, flow control, congestion control
Application Layer: Application specific – display/presentation
  Functions: Synchronization/timing, error recovery

## Slide 46: IEFT Protocol Stack Example
00:20:af:03:98:28
0a:e8:b7:46:19:50
Port 80
Port 2531
128.143.137.144
128.143.71.21
00:e0:f9:23:a8:20
00:10:25:ae:a3:40
application
transport
network
link
Process ID
Process ID
Request

## Slide 47: Protocols in Action
47
Send HTTP Request to neon
Establish a connection to 128.143.71.21 at port 80
Open TCP connection to 128.143.71.21 port 80
Send a datagram (which contains a connection request) to 128.143.71.21
Send IP datagram to 128.143.71.21
Send the datagram to 128.143.137.1
Send IP data-gram to 128.143.71.21
Send Ethernet frame to 00:20:af:03:98:28
Send Ethernet frame to 00:e0:f9:23:a8:20
Send the datagram to 128.143.7.21
Frame is an IP datagram
Frame is an IP datagram
IP datagram is a TCP segment for port 80
IP Router
Port 2531
Port 80
0a:e8:b7:46:19:50
00:20:af:03:98:28
128.143.137.144
128.143.137.1
128.143.71.21
00:e0:f9:23:a8:20
00:10:25:ae:a3:40

## Slide 48: Encapsulation
with layering comes encapsulation
each layer adds control bits used to perform its function related to the data exchange
the packet grows in size as it flows from application layer to datalink layer at the source
the packet is stripped of bits at the destination as it travels back up the stack from datalink layer to the application layer

## Slide 49: IETF Encapsulation
transport layer segment with header Ht
network layer datagram with header Hn
link layer frame with header Hl and trailer Tl
linkh
networkh
transporth
linkt
message

## Slide 50: Example
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
M
Ht
M
M
message
M
Ht
M
Ht
Hn
Hl
M
frame
Tl
Hx: header
Tx: trailer
M: message
X: t - transport, n - network, l - link
Internet
Ht
Hn
Hl
M
Tl

## Slide 51: Example
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
M
Ht
Hn
M
router
switch
message
M
Ht
M
Hn
Ht
Hn
Hl
M
frame 1
Tl
Ht
Hn
Hl
M
frame 1
Tl
Ht
Hn
Hl
M
frame 2
Tl
Ht
Hn
Hl
M
frame 1
Tl
Ht
Hn
Hl
M
frame 1
Tl
X
Hx: header
Tx: trailer
M: message
X: t - transport, n - network, l - link

## Slide 52: Chapter 1: roadmap
  1.0 a little history
  1.1 what is the Internet?
  1.2 network core - packet switching
  1.3 the global Internet infrastructure
  1.4 network architecture - protocol layers
  1.5 a primer on Internet addressing
  1.6 networks under attack - security
Notes: 52

## Slide 53
Each device on the Internet needs an address to allow a source to reach a destination for data retrieval and transmission.
Working with the IEFT model, we identify different levels of addressing:
  network device on a network – network address
  physical device on link – hardware address
Why two addresses?
  Because of shared medium physical layers
    many devices using the same link
    have to identify the network interface card of the device you are trying to reach
  Point to point, e.g., serial link, h/w address it is not necessary, link protocol does not use it
How do we find a “device”

## Slide 54: Network and H/W Addressing
each device connects to a network via an interface
interface: connection between host/router and physical link
  routers typically have multiple interfaces (>one)
    each interface creates a distinct/separate network
  hosts typically have one or two interfaces (e.g., wired Ethernet, wireless 802.11)
    interfaces may or may not be on a same network
each interface has
  a network address and
  a hardware address
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
00:e0:f9:23:a8:20
00:20:af:03:98:28

## Slide 55: What is a Network address?
network address is usually referred to as the IP (Internet Protocol) address
henceforth we will refer to it as IP address
an IP address is a unique global address for a network device
in the labs we will primarily be using IPv4 addresses
an IP (v4) address:
  is a 32 bit long identifier – 4bytes separated by dots
  IPv4 uses CIDR notation – Prefixes indicate the network portion of the address, ie the network number
    the network number is assigned by a global organization
  the remaining bits identify the host number
    the host number is assigned locally in each network
human analogy:
  network number  ``street name, city, state, country’’
  host number  house number

## Slide 56: IPv4 Dotted Decimal Notation
IP addresses are written in a dotted decimal format
each byte is identified by a decimal number in the range [0….255] – 28
Example: 128.143.137.144/16
  the number after the “/” is the prefix number/length, which identifies the network portion of the address (network prefix)
10001111
10000000
10001001
10010000
1st Byte
= 128
2nd Byte
= 143
3rd Byte
= 137
4th Byte
= 144
128.143.137.144
network host

## Slide 57: IPv6 Addresses
IPv6 addresses are huge – 128bits long!!!
IPv6 addresses use hexadecimal notation with colons -> abbreviation rules are used to shorten notation
IPv6 uses CIDR notation -> prefixes
structure of an IPv6 address is complex and identifies type of address
IPv6 address includes the MAC/hardware address

## Slide 58: Notation of IPv6 addresses
IPv6 addresses are written as hexadecimals
  “Blocks” of 16 bits are separated by colons
abbreviation is used to simplify notation

## Slide 59: Abbreviation Rules
leading zeros in a block can be omitted
one (but only one) group of contiguous blocks with all zeros can be replaced by a double colon
FE80:0000:0000:0000:002A:0000:0000:0A81
FE80:0:0:0:2A:0:0:A81
FE80:0:0:0:2A:0:0:A81
FE80::2A:0:0:A81
FE80:0:0:0:2A::A81
FE80::2A:0:0:A81
Best abbreviation yields the correct notation:

## Slide 60: CIDR Notation for IPv6 Addresses
IPv6 addresses are written in CIDR notation
    2607:F2C0:92C7:4A00:1053:D1D:66E9:41EA/64
The number after the slash (/) is the prefix length, which identifies the network part (network prefix)
all interfaces on the same network have the same network prefix
the only differences to IPv4 are the hex notation and the length of the addresses (and abbreviation)
1053:D1D:66E9:41EA
2607:F2C0:92C7:4A00
prefix length
128 bits
64 bits
64 bits

## Slide 61: Chapter 1: roadmap
  1.0 a little history
  1.1 what is the Internet?
  1.3 network core - packet switching
  1.5 the global Internet infrastructure
  1.4 network architecture - protocol layers
  1.5 a primer on Internet addressing
  1.6 networks under attack - security
Notes: 61

## Slide 62: Network security
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!

## Slide 63: Bad guys: put malware into hosts via Internet
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam. DDoS attacks

## Slide 64
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
2. break into hosts around the network (see botnet)
3. send packets to target from compromised hosts
Bad guys: attack server, network infrastructure

## Slide 65: Bad guys can sniff packets
packet “sniffing”:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  wireshark software used for end-of-chapter labs is a (free) packet-sniffer

## Slide 66
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Physical
application
(www browser,
email client)
application
OS
packet
capture
(pcap)
packet
analyzer
copy of all Ethernet frames sent/received

## Slide 67: Bad guys can use fake addresses
IP spoofing: send packet with false source address
A
B
C
src:B dest:A payload
… lots more on security (throughout, Chapter 8)